SECTION 10705

EXTERIOR SUN CONTROL DEVICES

Display hidden notes to specifier by using "Tools"/"Options"/"View"/"Hidden Text".

** NOTE TO SPECIFIER ** Ruskin Company; sun control devices.
 .
 This section is based on the products of Ruskin Company, which is located at:
3900 Dr. Greaves Rd.  
Grandview, MO 64030
Tel: 816-761-7476
Fax: 816-765-8955
Email: request info
Web: www.ruskin.com 
[ Click Here ] for additional information.
 
 Ruskin Sunshades offer energy savings by reducing solar heat gain through glazing. With a wide variety of available blade styles and configurations, they also provide aesthetic appeal to the building exterior. Ruskin Sunshade models include airfoil, louver, tube and eggcrate blade styles. Custom Sunshade designs are also available. Ruskin Sunshades are constructed of aluminum components for reduced weight and excellent corrosion resistance. All models are available with several Kynar finishes.

PART 1    GENERAL

1.1	SECTION INCLUDES

A.	Exterior sun control shades.

1.2	RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

A.	Section 03300 - Cast-In-Place Concrete.

B.	Section 04200 - Masonry Units.

C.	Section 05100 - Structural Metal Framing.

D.	Section 06100 - Rough Carpentry.

E.	Section 07600 - Flashing and Sheet Metal.

F.	Section 07920 - Joint Sealants.

1.3	REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

A.	AAMA 2605 - High Performance Organic Coatings on Architectural Extrusions and Panels.

B.	AAMA 2604 -  High Performance Organic Coatings on Architectural Extrusions and Panels.

C.	ASCE 7 - Minimum Design Loads for Buildings and Other Structures.

D.	ASTM B209 - Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate.

E.	ASTM B221 - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes.

F.	ASTM D4214 - Standard Test Methods for Evaluating the Degree of Chalking of Exterior Paint Films.

G.	ASTM D2244 - Standard Test Method for Calculation of Color Differences From Instrumentally Measured Color Coordinates.

1.4	PERFORMANCE REQUIREMENTS

** NOTE TO SPECIFIER **  Confirm code mandated requirements. ASCE values in lieu of code mandated requirements may be used. Delete if not required.

A.	Sun shades shall be factory engineered to withstand wind loads, acting inwards and outwards.

1.	Minimum design loads shall be calculated to comply with ASCE -  7, or local requirements of Authority Having Jurisdiction.

** NOTE TO SPECIFIER **  Confirm code mandated requirements. ASCE values in lieu of code mandated requirements may be used. Delete if not required.

B.	Sun shades shall be factory engineered to withstand the specified seismic loads.

1.	Minimum design loads shall be calculated to comply with ASCE -  7, or local requirements of Authority Having Jurisdiction.

** NOTE TO SPECIFIER **  Confirm delta- T anticipated. Delete if not required.

C.	Sun shades shall be factory engineered to withstand the thermal stress to which the louvers will be subjected.

1.	Base engineering on a surface design temperature change of 180 degrees F (82 degrees C).

D.	Sun shades shall be designed to perform under conditions specified herein or required by site conditions with no permanent damage to or deforming of the louver blades or assembly, noise or metal fatigue caused by louver blade rattle or flutter, or permanent damage to fasteners and anchors.

1.5	SUBMITTALS

A.	Submit under provisions of Section 01300.

B.	[ Product Data ]:  Manufacturer's data sheets on each product to be used, including:

1.	Preparation instructions and recommendations.

2.	Storage and handling requirements and recommendations.

3.	Installation methods.

C.	Shop Drawings: Indicate adaptation of manufacturer's standard sun shade system to Project; system elevations, and dimensions, structural support requirements and tolerances, profiles of members, anticipated deflection under load and details.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

D.	Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

E.	Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) square, representing actual product, color, and patterns.

1.6	QUALITY ASSURANCE

A.	Obtain sunshade systems from one source, from a single manufacturer.

B.	Sunshade systems shall be manufactured by a firm with a minimum of 5 years of experience in the design, engineering and fabrication of similar systems.  Alternate manufacturers shall submit evidence of sufficient expertise and experience no less than 10 days prior to bid date.  If such manufacturers are judged acceptable, they will be identified by addendum prior to bid date.  No other form of approval shall be acceptable.

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Store products in manufacturer's unopened packaging until ready for installation.

B.	Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of local authorities having jurisdiction.

1.8	PROJECT CONDITIONS

A.	Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

B.	Installer shall verify actual measurements/connections by field measurements before fabrication; show recorded measurements on shop drawings.  Coordinate field measurements and fabrication schedule with construction progress to avoid construction delays.

1.9	WARRANTY

A.	Manufacturer shall provide standard limited warranty for sunshade systems for a period of 1 year from date of installation, no more than 18 months after shipment from manufacturing plant. When notified in writing from the Owner of a manufacturing defect, manufacturer shall promptly correct deficiencies without cost to the Owner.

B.	Manufacturer shall provide 20 year limited warranty for Kynar-based finish.

PART 2    PRODUCTS

2.1	MANUFACTURERS

A.	Acceptable Manufacturer: Ruskin Company, which is located at: 3900 Dr. Greaves Rd.  ; Grandview, MO 64030; Tel: 816-761-7476; Fax: 816-765-8955; Email: request info; Web: www.ruskin.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

B.	Substitutions:  Not permitted.

C.	Requests for substitutions will be considered in accordance with provisions of Section 01600.

2.2	DESIGN

A.	Refer to Drawings for application, design and details.

** NOTE TO SPECIFIER **  Delete pre-engineered design if not required.

B.	Pre-engineered application:

** NOTE TO SPECIFIER **  Delete design not required.

1.	Horizontal cantilever.

2.	Horizontal supported.

3.	Vertical hung.

** NOTE TO SPECIFIER **  Delete custom design reference if not required.

C.	Custom application as indicated and detailed on drawings.

2.3	COMPONENTS

A.	Blade Design: 6063T5 alloy extruded aluminum.

** NOTE TO SPECIFIER **  Delete louver blade design not required.

1.	Louver blade, horizontally mounted, SSLBH4, 4 inch (102 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 37-1/2 degree angle.

2.	Louver blade, horizontally mounted, SSLBH6, 6 inch (152 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 37-1/2 degree angle.

** NOTE TO SPECIFIER **  Delete air foil blade design not required.

3.	Airfoil blade, horizontally mounted, SSAFH4, 4 inch (102 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 45 degree angle.

4.	Airfoil blade, horizontally mounted, SSAFH6, 6 inch (152 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 45 degree angle.

5.	Airfoil blade, horizontally mounted, SSAFH8, 8 inch (203 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 45 degree angle.

6.	Airfoil blade, vertically mounted, SSAFV4, 4 inch (102 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 45 degree angle.

7.	Airfoil blade, vertically mounted, SSAFV6, 6 inch (152 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 45 degree angle.

8.	Airfoil blade, vertically mounted, SSAFV8, 8 inch (203 mm) blade width.

a.	0.081 inch (2.1 mm) nominal thickness, installed at 45 degree angle.

** NOTE TO SPECIFIER **  Delete rectangular tube blade design not required.

9.	Rectangular tube blade, horizontally mounted, SSRTH4, 4 inch (102 mm) blade width.

a.	1-3/4 inches by 4 inches by .125 inch (44 mm by 102 mm by 3.2 mm) installed at 45 degree angle and 4-1/2 inches (114 mm) center-to-center spacing.

10.	Rectangular tube blade, horizontally mounted, SSRTH6, 6 inch (152 mm) blade width.

a.	2 inches by 6 inches by .125 inch (51 by 152 by 3.2) installed at 45 degree and 6 inches (152 mm) center-to-center spacing.

11.	Rectangular tube blade, vertically mounted, SSRTV4, 4 inch (102 mm) blade width.

a.	1-3/4 inches by 4 inches by .125 inch (44 mm by 102 mm by 3.2 mm) installed at 45 degree angle and 4-1/2 inches (114 mm) center-to-center spacing.

12.	Rectangular tube blade, vertically mounted, SSRTV6, 6 inch (152 mm) blade width.

a.	2 inches by 6 inches by .125 inch (51 by 152 by 3.2) installed at 45 degree and 6 inches (152 mm) center-to-center spacing.

** NOTE TO SPECIFIER **  Delete eggcrate blade design not required.

13.	Eggcrate blade, horizontally mounted, SSEGH2, 2 inch (51 mm) deep eggcrate.

14.	Eggcrate blade, horizontally mounted, SSEGH4, 4 inch (102 mm) deep eggcrate.

15.	Eggcrate blade, horizontally mounted, SSEGH6, 6 inch (152 mm) deep eggcrate.

16.	Eggcrate blade, vertically mounted, SSEGV2, 2 inch (51 mm) deep eggcrate.

17.	Eggcrate blade, vertically mounted, SSEGV4, 4 inch (102 mm) deep eggcrate.

18.	Eggcrate blade, vertically mounted, SSEGV6, 6 inch (152 mm) depth.

** NOTE TO SPECIFIER **  Eggcrate dimensions of 2 inches to 12 inches (51 mm to 305 mm) width by 2 inches to 12 inches (51 mm by 305 mm) length.  Both grid dimensions must be at least as deep as the eggcrate depth.  Delete width and length not required.

19.	0.125 inch (3.2 mm) nominal thickness (305 mm).

20.	Grid Dimension - Width: 2 inches (51 mm).

21.	Grid Dimension - Width: 3 inches (76 mm).

22.	Grid Dimension - Width: 4 inches (102 mm).

23.	Grid Dimension - Width: 5 inches (127 mm).

24.	Grid Dimension - Width: 6 inches (152 mm).

25.	Grid Dimension - Width: 7 inches (178 mm).

26.	Grid Dimension - Width: 8 inches (203 mm).

27.	Grid Dimension - Width: 9 inches (227 mm).

28.	Grid Dimension - Width: 10 inches (254 mm).

29.	Grid Dimension - Width: 11 inches (279 mm).

30.	Grid Dimension - Width: 12 inches (305 mm).

31.	Grid Dimension - Length: 2 inches (51 mm).

32.	Grid Dimension - Length: 3 inches (76 mm).

33.	Grid Dimension - Length: 4 inches (102 mm).

34.	Grid Dimension - Length: 5 inches (127 mm).

35.	Grid Dimension - Length: 6 inches (152 mm).

36.	Grid Dimension - Length: 7 inches (178 mm).

37.	Grid Dimension - Length: 8 inches (203 mm).

38.	Grid Dimension - Length: 9 inches (227 mm).

39.	Grid Dimension - Length: 10 inches (254 mm).

40.	Grid Dimension - Length: 11 inches (279 mm).

41.	Grid Dimension - Length: 12 inches (305 mm).

B.	Fascia Profile: Size as indicated on Drawings.

** NOTE TO SPECIFIER **  Delete fascia profile not required.

1.	Channel.

2.	Round.

C.	Outrigger Profile: Size as indicated on Drawings.

** NOTE TO SPECIFIER **  Delete outrigger profile not required.

1.	Straight.

2.	Tapered.

3.	Channel.

2.4	FINISHES

** NOTE TO SPECIFIER **  Delete type of Kynar finish not required.

A.	Finish:  70 percent Kynar-Based Painted Finish.

1.	Coating shall conform to AAMA 2605. Apply coating following cleaning and pretreatment. Cleaning:  AA-C12C42R1X.

2.	Standard 2-coat Kynar 500.

3.	Pearledize 70 (2-coat mica).

4.	3-coat metallic.

5.	3-coat exotic Kynar.

B.	Finish:  50 percent Kynar-Based Painted Finish.

1.	Coating shall conform to AAMA 2604, sections 4.2 and 4.3. Apply coating following cleaning and pretreatment. Cleaning:	AA-C12C42R1X.

2.	Baked Enamel.

3.	Pearledize 50 (2-coat mica).

PART 3    EXECUTION

3.1	EXAMINATION

A.	Do not begin installation until substrates have been properly prepared.

B.	If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

3.2	PREPARATION

A.	Clean surfaces thoroughly prior to installation.

B.	Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

3.3	INSTALLATION

A.	Install in accordance with manufacturer's instructions.

3.4	PROTECTION

A.	Protect installed products until completion of project.

B.	Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION